## Slide 1
Advanced Predictive Modeling and Optimization for Silicon (SI) Content in Hot Metal
Objective:
Silicon (SI) content in hot metal serves as a fundamental indicator of blast furnace thermal stability, playing a pivotal role in operational efficiency and safety. This approach outlines a comprehensive Artificial Intelligence and Machine Learning (AI/ML)-driven solution designed to predict SI content with high accuracy, integrate real-time anomaly detection, facilitate preemptive root cause analysis, and enable dynamic furnace parameter optimization.

## Slide 2
Metadata
Feature Name | Category | Description/Relevance to SI Prediction | Data Type
Timestamp | Time-Series | Enables time-series analysis, trend identification, and sequence modeling. Crucial for understanding temporal dependencies and delays. | Timestamp
OxEnRa | Operating Parameter | Oxygen Enrichment Rate: Influences combustion efficiency and thermal state, directly impacting Si levels. | Numerical
BlFuPeIn | Operating Parameter | Blast Furnace Permeability Index: Reflects gas flow resistance, impacting heat transfer and reduction reactions. | Numerical
EnOxFl | Operating Parameter | Enriched Oxygen Flow: Direct input affecting fuel combustion and overall thermal energy. | Numerical
CoBlFl | Operating Parameter | Cold Blast Flow: Affects the volume and temperature of air entering the furnace, influencing thermal state. | Numerical
BlMo | Operating Parameter | Blast Momentum: Relates to the kinetic energy of the blast, impacting raceway conditions and heat distribution. | Numerical
BlFuBoGaVo | Operating Parameter | Blast Furnace Bottom Gas Volume: Indicator of gas flow and reactions in the lower part of the furnace. | Numerical
BlFuBoGaIn | Operating Parameter | Blast Furnace Bottom Gas Index: Reflects gas composition and efficiency of reduction reactions. | Numerical
ThCoTe | Operating Parameter | Theoretical Combustion Temperature: Key indicator of thermal energy within the furnace, strongly correlated with Si content. | Numerical
ToGaPr | Operating Parameter | Top Gas Pressure: Influences gas flow dynamics and burden descent. | Numerical
EnOxPr | Operating Parameter | Enriched Oxygen Pressure: Related to oxygen supply and its impact on combustion. | Numerical
CoBlPr | Operating Parameter | Cold Blast Pressure: Indicates resistance to blast flow, affecting furnace stability. | Numerical
ToPrDr | Operating Parameter | Top Pressure Drop: Reflects gas flow resistance in the upper furnace, related to burden permeability. | Numerical
HoBlPr | Operating Parameter | Hot Blast Pressure: Pressure of the hot air injected, impacting penetration and reaction zones. | Numerical
AcBlVe | Operating Parameter | Actual Blast Volume: Total volume of hot blast injected, a major control parameter for thermal state. | Numerical
CoBlTe | Operating Parameter | Cold Blast Temperature: Temperature of air before heating, impacts hot blast temperature. | Numerical
HoBlTe | Operating Parameter | Hot Blast Temperature: Direct input affecting the thermal state and energy balance of the furnace. | Numerical
ToTe | Operating Parameter | Top Temperature: Reflects gas distribution and heat exchange in the upper stack. | Numerical
BlHu | Operating Parameter | Blast Humidity: Water vapor content in blast, impacts hydrogen content and coke rate. | Numerical
CoInSeVa | Operating Parameter | Coal Injection Set Value: Amount of pulverized coal injected, a critical fuel and reductant. | Numerical
FoSI | Process Output | Fomer SI: Potentially a previous model's forecast, could be used as a feature or for comparison. | Numerical
HoBl | Operating Parameter | Hot Blast: Likely related to hot blast flow or volume, impacting thermal state. | Numerical
ToGasP | Operating Parameter | Top Gas Pressure: Pressure of gas exiting the furnace, related to burden movement. | Numerical
CoBF | Burden Composition | Coke Burden Factor: Ratio of coke in the burden, directly influencing thermal input and reduction. | Numerical
SI | Target Variable | Silicon content in hot metal: The primary output to be predicted, critical for thermal stability. | Numerical

## Slide 3
Objectives:
High-Performance Predictive Model for SI, optimized for accuracy and robustness.
Tried different models ranging from Linear models to Tree based ensemble models. Was not
able to achieve good accuracy with the current dataset but tree based models were more
accurate.
In tree based models, even though boosting models like XGB and LightGBM were able to
provide more accuracy but I finally went with Random Forest. Random forest had
comparable accuracy and is not affected by hyper parameter tuning, hence more robust.
Getting final accuracy of: MAPE : 13.9386%
RMSE : 0.0813
R-Squared : 0.3789

## Slide 4
B. Provision Real-time Anomaly Detection to flag unexpected SI deviations and recommend corrective actions.
C. Preemptive Root Cause Analysis to identify key parameters affecting SI and guide process control decisions.
Explainability & Actionability: SHAP analysis, feature importance, and business-relevant insights for furnace optimization.
D. Comprehensive Model Evaluation:
Performance Metrics: R², RMSE, MAPE.
Uncertainty Quantification for confidence estimation.
Robustness Testing to validate performance under varying process conditions.
I’ve tried these in post modeling notebook

## Slide 5
G. Scalable Deployment Strategy:
Real-time inference with low-latency processing.
Model Drift Detection & Retraining Mechanism for sustained performance.
Cloud or Edge Deployment Considerations based on operational constraints.
Hypothesis: Assuming that the output of SI prediction, anomaly detection, root cause
analysis and corrective action recommendation will be utilized by operators/engineers on Blast
Furnace plant premise.
And their actions will be critical and time dependent for blast furnace operation.
Here is the Flow I assume: Data Source → API Gateway → Model Service → Alert System → Operator Dashboard (Sensors) (REST API) (Flask/FastAPI) (Notifications) (Web Interface)
So for Real-time inference with low-latency processing, we will go with-
EDGE deployment(means running your ML model as close as possible to where the data is
generated) Instead of Cloud Deployment
Which is ideal for this case as:
Reliability: Works without internet
Security: Data stays on-premises
Cost: No cloud computing fees for inference
Speed: No internet round-trip

## Slide 6
Further for Model Drift Detection & Retraining Mechanism for sustained performance
We can go on cloud based architecture.
Data pipeline in this case will look something like this:
Edge Server → Periodic Data Upload → Cloud Storage
(Daily/Weekly) (Historical data) (Data Lake Azure/GCP/AWS)
This can help with:
Model versioning
Performance monitoring
Model drift detection
Retraining with new data

## Slide 7
Deployment strategy with key infrastructure and integration details:
Architecture overview
HYBRID EDGE-CLOUD DEPLOYMENT:
With EDGE Layer sitting on premise on steel plant providing real-time model results.
And Cloud Layer sitting on cloud for Model lifecycle
B. Edge Infrastructure (Real-Time Operations)
Location: On-premises at steel plant
Components:
Model Serving: Containerized ML models (Docker)
API Layer: FastAPI/Flask for real-time inference
Data Processing: Stream processing for sensor data
Alert System: Real-time anomaly notifications
Local Storage: Redis cache for recent predictions
C. Cloud Infrastructure (Model Management) Purpose: Model lifecycle and analytics Components:
Model Training: Automated ML pipelines with Databricks and Azure Data Factory/AWS Glue for orchestration
Drift Detection: Statistical monitoring services with pipeline-based triggers and automated alerts
Data Lake: Historical performance data on Azure Data Lake/AWS S3 with time-series partitioning
Model Registry: Version control and deployment management via MLflow/Azure ML integrated with GitHub/Bitbucket